## Slide 1: Maximize Output from Solar Hybrid Solutions
By: Dinesh Kaul
Control Electric Co. Pvt. Ltd.
33rd ISA SUNMEET
On
“Solar Hybridisation of Diesel Gensets”

## Slide 2: Agenda
About Us
Why Hybrid ?
Standard HySPP
Issues with Standard HySPP
Extract Maximum Output of HySPP
Battery Efficiency & Consumption
Modular, Scalable & Flexible
DG-PV Synchronization
Summary

## Slide 3: About Us
25 Years of experience in Electrical , Automation, Solar (Since 2014)
ISO Certified | MNRE Channel Partner| MSME Approved| CPRI Approved
India, Malaysia, Nepal, Bangladesh, Sri Lanka & Philippines
Schneider Solar Value Added Distributor
Complete End To End Solution Provider

## Slide 4: Why Hybrid ?
Always have power in any situation.
Off Grid Wastes Power generated but not Consumed
Power is
    Discom @ Rs.10/Unit ($ 0.13/KWh)
    Diesel generators @ Rs. 22/Unit ($ 0.30/KWh)
    Hybrid SPP @ Rs.12/Unit ($ 0.16/KWh)
Excellent Return on your Money - Better than Banks and Mutual Funds

## Slide 5: Standard Hybrid SPP
Diesel Generator
50 Kw
Solar PV
50 KWp
Grid
50 KW
Hybrid Inverter
50 KW
AC Distribution
Battery: 4 Hrs
Load: 50 KW

## Slide 6: Issues with Standard HySPP
Battery Not Getting Charged Fully by PV
Not Suitable for Surge Load
Optimal System Design
  AC Coupling
  DC Coupling
  AC-DC Coupling
Sync. With Existing Electrical Infra
Retrofitting with existing SPP
Design Optimization

## Slide 7: Retrofitting With Existing Power Plant

## Slide 8: Extract Maximum Output of your HySPP
Design as per Load Profile
  AC Coupled for day load : Sync with Existing SPP
  DC Coupled for night load : Without Sync
  AC-DC Coupled for day & night load
AC Coupled System vs DC Coupled System (50 KW) with 50 Kw of DG(Running 4 Hrs/day)
Type | DC Coupled System | AC Coupled System
Investment | Rs. 10,265,000 U$D 142,570 | Rs.1,0025,000 U$D 139,000
Savings @ 4 Hr. DG running in 15 Year | Rs. 25,180,000 U$D 349,000 | Rs. 25,180,000 U$D 349,000
Return of Investment | 6.1 Years | 5.9 Years

## Slide 9: Peak Shaving
Use HySPP for avoids new investments on DG/Transformer
Use for Peak Shaving
MDI Controller
Time of the Day
Improve DG Effi.

## Slide 10: Extract DG Efficiency
Increase the efficiency of DG.
Charge Batteries when Load is Low

## Slide 11: Selection of Battery
Selection of Battery as per nature of Load
Li-Ion
Fast discharging e.g. Peak Shaving/MDI Control
Space Constraint e.g. Bank ATM
Life Cycle req. needs to be high e.g. Remote Area
Fast Charging is Req. e.g. Hospitals
Lead Acid
Discharge rate ≃ C/10
Upfront Price is bigger
Other Chemistries Supported: Flow battery, Aluminium Ion, Lithium Metal, Nickel–cadmium, Sodium–sulfur battery, etc.

## Slide 12: Battery Efficiency & Consumption
Consider Inverter & Battery efficiency @high temperatures
Consider Inverter & Battery efficiency @low temperatures
Idle Consumption
Description | Standard Inverter | Good Inverter
Idle Consumption of Inverter | 900 W | 63 W
Idle for 12.00 Hrs: Power Required | 10800 W | 756W
Battery Required to provide power to Inverter in Idle mode | 15.00 KWh | 1.05 KWh
Total Gain in 15 Years 50 KW |  | Rs. 10,19,993 U$D 14167

## Slide 13: Safe Voltage
48V is reasonably safe for most people under normal conditions.
48V is the practical and LEGAL definition of the maximum voltage to be considered "low voltage" and intrinsically "safe".
Certainly 48V delivered UNDER your relatively insulating skin surface could kill you if delivered in the "right" place. But we are assuming people aren't walking around with subcutaneous electrodes exposed to accidental contact with "LV" wiring.

## Slide 14: Modular, Scalable & Flexible
Inverter Ratings (6 KW) | Standard Inverter | Good Inverters
Battery (Max.) | 400 AH | 10,000 AH
PV Connectable (Max.) | 5 KWp | 72 KWp

## Slide 15: Modular, Scalable & Flexible
Hybrid Solar Power plant is flexible to sync Power with
Diesel Generators
BioGas
Grid Power Supply
Wind Power Supply
Battery Storage

## Slide 16: DG - PV Synchronization
Case | Available Solar Power (50 KW) | Load on 50kW Diesel Generator | Customer Load | Load on Solar
2:00 PM | 50 | 15 | 35 | 70%
3:00 PM | 40 | 15 | 45 | 60%
4:00 PM | 30 | 15 | 30 | 30%
6:00 PM | 20 | 15 | 20 | 10%

## Slide 17: Summary
HySPP is be Modular, Flexible and Scalable
Power Output: 6 Kw to 72 Kw
Battery Backup: 1 Hour to 10 Hour.
Solar PV Module: 3.5 KWp- 225 KWp
IIoT Hardware, Industry 4.0 enabled for Control & Monitoring
Remotely manage:
  System settings
  Firmware updates
Segregate Load
  Emergency Load
  Non-Emergency Load

## Slide 18
Thank You
Save Money. Save Earth. Save Environment.