## Slide 1: Renewable Energy
Wind & Solar

## Slide 2: KERALA
Wind
Solar
100 MW
 | Solar | Wind | Total- RE
Existing | 134 | 70 | 204
Upcoming | 1392 | 140 | 1532
Total | 1526 | 210 | 1736
100MW
500 MW
250 MW
250 MW

## Slide 3: SOLAR
Existing |  | Ongoing Projects |  | Upcoming Proposals | 
Owned | MW | Owned | MW | Soura | MW
KSEBL | 16.41 | KSEBL | 17.86 | Roof Top | 500
CIAL | 30 | NHPC-Kallada Floating | 50 | Ground mounted | 
IREDA | 50 | KMRL | 5.348 | Floating solar | 100
ANERT | 2 | HINDALCO | 4 | Canal top | 50
HINDALCO | 1 | BPCL | 4 | Solar park | 150
Grid connected Consumers | 34.19 | KTDC | 3 | Procurement through PPA | 200
 |  | Bharath Charitable Hospital Society | 1.1 | NTPC-floating | 92
 |  |  |  | NTPC-ground mounted | 15
 |  |  |  | SECI | 200
TOTAL | 133.61 | TOTAL | 85.308 | TOTAL | 1307

## Slide 4
Sources | Installed capacity in MW
Hydel | 2052
Thermal | 510
Wind | 70
Solar | 134
Others | 20
Total | 2786
INSTALLED CAPACITY OF VARIOUS SOURCES OF GENERATION IN KERALA

## Slide 5
HIGHEST DEMAND MET IN MW | HYDRO -GEN | CGS | LTA | PURCHASE POWER EXCHANGE | SWAP | UI
4345 | 1660 | 1242 | 1046 | 182 | 195 | 20
HIGHEST CONSUMPTION | Hydel | CGS | LTA | PX | SWAP | Wind | Solar | UI
88.1 | 24.46 | 30.39 | 25 | 5.12 | 2.34 | 0.098 | 0.38 | 0.312
% | 28% | 34.44% | 27.78% | 5.89% | 3% | 0.11% | 0.43% | 0.35%

## Slide 6: WIND
Existing |  | Ongoing Projects | 
Owned | MW | Owned | MW
KSEBL | 2.025 | KSEBL | 6
IPP | 58.25 | Reverse Bidding | 50
CPP-Manorama | 10 | NHPC-(Idukki & Palakkad) | 82
 |  | Ramakkelmedu | 2
TOTAL | 70.28 | TOTAL | 140

## Slide 7
The project is India’s largest floating solar power plant.
500 kWp (kilowatt peak) solar plant floats on 1.25 acres of water surface of the reservoir.
1,938 solar panels installed on 18 ferro cement floaters with hollow insides.
Cost of Rs 9.25 crore.
Floating substation have been set up on the reservoir itself to convert the output into 11kV, considering economic and safety aspects.
A 500 KVA (Kilo volt ampere) transformer, 17 inverters, a supervisory control and data acquisition (SCADA) system to control and monitor power generation and an anchoring system.
Generates 7.5 lakh units of power annually which will be fed to the KSEB grid using underwater cables.
KSEB Ltd
BANASURA SAGAR DAM
SOLAR PROJECT
Padinjarathara, Wayanad District
Kerala State

## Slide 10
Ferrocement floats - 18 nos
Solar PV pannels - 1938 nos
(260 kWp)
Transfor – 500 kVA,11KV/415V
Inverters – 30 kW X 17 nos
Banasura saagar
500 kW
Ferrocement floating platform

## Slide 11
Completed projects- Padinjarethara dam top- 440kW
Padinjarethara dam top- 440kW
Dam top -285m and 8m width
Completed on 19.05.2016
Contractor - M/s KELTRON
State fund- Rs. 3.425 Crore
Commissioned on 29.08.2016
Note: Largest dam top project in India
Notes: 11

## Slide 12: 440 kWp DAM TOP SOLAR PLANT AT PADINJARETHARA

## Slide 13: Padinjarethara- Banasurasagar 440 kWp Dam Top

## Slide 14
Ongoing projects- Barapole 3MW canal top
Barapole Canal Top – 3 MW
‘Pilot-cum-Demonstration
Project for Development of
Grid Connected
Solar PV Power Plants on
Canal Banks and Canal
Tops” of MNRE
Notes: 14

## Slide 15
Ongoing projects
Barapole canal -3MW
Barapole Canal Top – 3MW
Notes: 15

## Slide 16
Completed projects of KSEBL- Kanjikode - 1MW
Kanjikode - 1MW
Status: Completed on 10/8/2015
Own land - 5 Acres
Contractor - M/s Bosch Ltd.,
Bangalore
Project cost/ Contract amount -
Rs. 8Crore
Average Monthly generation –
Units -0.12 MU
Note: First utility scale
ground mounted project
of KSEBL

## Slide 17
Completed projects –Agali Tribal colony
Agali tribal colony- 96kW
Status: commisioned
Colony consisting of 74 houses
Commissioned on 31.08.2015
Contractor – M/s KELTRON
Funded by – Govt of Kerala
Project cost/ Contract amount – Rs.109.45 Crore
Average Monthly generation – 7770units
Note: Socially obligatory roof top solar programme

## Slide 18
Present Agali Tribal colony-100kWp(92 Houses) w.e.f 2015
Consumption of colony free of cost for 25 years
Remaining purchased by KSEBL
Purchased amount utilised for the welfare of the colony and remaining for O&M of SPV project

## Slide 19
SOURA
  Launched by Govt of Kerala
  1000 MW solar power in the next 3 years
500 MW Rooftop and Ground mounted
200 MW to be procured through PPA
100 MW floating solar
50MW canal top
150MW Solar Park

## Slide 20: SOURA PROJECT
Online Registration : KSEB website
Current Registrations: 2.78L

## Slide 21: SOURA SCHEME MODELS FOR CONSUMERS
The RT/ land of consumers utilized for installing solar plant. Energy generated will be fed into the grid for a period of 25 years and a fixed percentage of generation will be given as the incentive/lease rent to the consumer for his own use.
KSEBL/ANERT will install RT/GM plant in consumer premises and the energy generated will be sold to the consumer for 25 years through PPA, as per his requirement at a fixed tariff.
The consumer will be the investor and KSEBL/ANERT will setup the solar plant for the consumer and excess energy if any after the consumption of consumer/ plant owner/ will be fed into KSEB’s grid at predetermined unit rate.

## Slide 22: Average Global Horizontal Irradiance, Kerala
Latitude: 10.85, Longitude: 76.25
Annual Average Global Horizontal Irradiance: 5.68 kWh/m2/day
Monthly Average : kWh/m2/day | 
JAN | 5.98
FEB | 6.51
MAR | 6.68
APR | 6.37
MAY | 5.90
JUN | 4.89
Monthly Average : kWh/m2/day | 
JUL | 4.74
AUG | 5.34
SEP | 5.67
OCT | 5.15
NOV | 5.39
DEC | 5.55

## Slide 23: SOURA : 1st phase
First phase tender :
  - 200MWp Rooftop/Ground mounted solar PV at various locations in the State in 2019-20
  Executing Agency:
  - SPV : JV of KSEBL & ANERT

## Slide 24: SOURA : 1st phase
Execution methodology :
  - Empanelment of EPC Contractors/Plant Developers
  Selection Criteria for empanelment :
    -EPC cost on per kWp/Levelized tariff basis or both
    Final call on selection through EPC or levelized tariff or both will be taken by bidding authority. It is desirable to quote on both basis.

## Slide 25
Financial Year | Minimum Non-Solar RPO target a % of Total Consumption excluding hydro generation |  | RPO Met | Minimum Solar RPO target a % of Total Consumption excluding hydro generation |  | RPO Met
 | % | MW(CUF- 25%) | MW | % | MW | MW
2018-19 | 7 | 497 | 273 | 2.75 | 257 | 116
2019-20 | 8 | 608 |  | 4 | 400 | 
2020-21 | 9 | 731 |  | 5.25 | 561 | 
2021-22 | 10.25 | 889 |  | 6.75 | 771 | 
RPO TARGETS

## Slide 26: RE- Southern India
State-IC | Solar | Wind | Total
AP | 2153 | 3948 | 6101
TL | 3362 | 101 | 3463
KAR | 4503 | 3908 | 8411
TN | 12028 | 16529 | 28557
KER | 134 | 70 | 204

## Slide 27
Thank You